## Slide 1: Mininet Tutorial
EL6363 Supplemental material for Lab 3

## Slide 2: Lab3 Objectives
Introduction to Software Defined Network
Master the simulation tool: mininet
Understand the operation of Openflow and observe its messages
Interfacing with Open Virtual Switch
Implement a simple flow-based routing algorithm

## Slide 3: Software Defined Network (SDN)

## Slide 4: Mininet
MiniNet creates scalable Software-Defined Networks (up to hundreds of nodes) using OpenFlow, on a single PC
It allows to quickly create, interact with and customize a software defined network prototype with complex topologies, and can be used to emulate real networks – all on your PC
MiniNet can work with any kind of OpenFlow controller
It takes seconds to install it
Easy to program
Of course, it is an open source project

## Slide 5: What does mininet provide?
Mininet emulates software defined networks.
Create virtual hosts and virtual switches
Test the connectivity and performance in a virtual environment
Mininet
Software Switch
Virtual Host
Virtual Host
Virtual Links

## Slide 6: Lab3 Overview (part 1)
Simulate a software defined network with 2 hosts and 5 switches
OVS A
OVS B
H2
H1
OVS C
OVS D
OVS E

## Slide 7: Lab3 Overview (part 1)
Implement flow-based routing instead of destination-based routing
  Traffic from H1  H2
    HTTP traffic with d_port=80, follow path: A-C-D
    other traffic, follow path: A-B-E-D
  Traffic from H2  H1
    HTTP traffic with s_port=80, follow path: D-B-A
    other traffic, follow path: D-C-E-B-A
Generate traffic and verify your result with Wireshark

## Slide 8: Lab3 Overview (part 2)
Given switches with N ports, create a 2-stage fat-tree topology with hosts in Mininet
  Make N an input parameter to your program (python script)
Ex:
sw
sw
sw
sw
sw
sw
sw
sw
sw
sw
sw
sw
sw
sw
sw
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
H
N=4
N=6

## Slide 9: Lab3 Steps
Install and run mininet
Follow mininet walkthrough and learn its commands
Capture OpenFlow messages passed through mininet hosts
Create a customized topology
Install custom forwarding rules on switches

## Slide 10: Installing mininet (Option 1) - recommended
Install a Ubuntu VM using either VMWare Player or VirtualBox
Install mininet through apt-get (remember to update first)
  sudo apt-get update
  sudo apt-get install mininet
Test installed mininet
  sudo mn --test pingall
To install default ovs controller
  sudo apt-get install openvswitch-testcontroller
  sudo cp /usr/bin/ovs-testcontroller /usr/bin/ovs-controller

## Slide 11: Installing mininet (Option 2)
Install a Ubuntu VM using either VMWare Player or VirtualBox
Follow the Option 2 instruction on http://mininet.org/download/
  git clone git://github.com/mininet/mininet
  mininet/util/install.sh [options]
  sudo mn --test pingall

## Slide 12: Installing mininet (Option 3)
Use a Linux VM Image that has mininet installed
Download the image from: http://mininet.org/vm-setup-notes/
Download and install VMWare Player or VirtualBox
  VMWare: https://my.vmware.com/web/vmware/free#desktop_end_user_computing/vmware_player/6_0
  VirtualBox: https://www.virtualbox.org/wiki/Downloads
Run the mininet VM using either program

## Slide 13: Running mininet
sudo mn --test pingall
S1
H2
H1
Controller

## Slide 14: Mininet Walkthrough
Follow the official mininet walkthrough & introduction
  http://mininet.org/walkthrough/
  https://github.com/mininet/mininet/wiki/Introduction-to-Mininet
Learn
  How to Run mininet, both
    Within mininet prompt
    With python scripts
  mininet’s basic commands
  Test connectivity between hosts

## Slide 15: Creating a custom topology
# Add hosts and switches
H1 = self.addHost( ‘H1' )
H2 = self.addHost( ‘H2' )
S1 = self.addSwitch( ‘S1' )
S2 = self.addSwitch( ‘S2' )
# Add links
self.addLink( H1 , S1 )
self.addLink( S1, S2 )
self.addLink( S2, H2 ) Refer to: https://github.com/mininet/mininet/blob/master/custom/topo-2sw-2host.py
S1
S2
H2
H1

## Slide 16: Manually installing rules on OVS nodes
In the lab we need these commands (you may need to sudo):
  ovs-ofctl show s1
  ovs-ofctl dump-flows s1
  ovs-ofctl add-flow s1 in_port=1,actions=output:2
  ovs-ofctl add-flow s1 priority=500,in_port=1,dl_type=0x0800,nw_proto=6,actions=output:2
Example:
For more details refer to: http://openvswitch.org/support/dist-docs/ovs-ofctl.8.txt http://www.pica8.com/document/v2.3/html/ovs-commands-reference/

## Slide 17: Running Mininet with Custom Topology
To launch Mininet with default controller:
  sudo mn --custom ~/mininet/custom/topo-2sw-2host.py --topo mytopo
before pingall
after pingall

## Slide 18: Running Mininet with Custom Topology
To launch Mininet without default controller:
  sudo mn --custom ~/mininet/custom/topo-2sw-2host.py --topo mytopo --controller remote
installing rules
before installing rules
after installing rules

## Slide 19: How to Run the Simulation
Use Mininet prompt
  Ex: sudo mn --custom ~/mininet/custom/topo-2sw-2host.py --topo mytopo --controller remote
  Giving parameter to mininet and enter a Mininet prompt
Put everything in a python script (Lab 3 Part 2)
  Ex: python myScript.py
  Putting everything in a python script, use python API to perform specific actions such as ping, iperf, ifconfig, etc …
For Lab 3 part 1, you can do it either way