## Slide 1: EL9333 – Lab 5

## Slide 2: Objectives
Fully understand the operation of OpenFlow and observe the operations
Learn basic skill of configuring an OpenFlow Switch
Trigger and observe the behavior of flow table overflow
Learn to manage flows based on limited network resources

## Slide 3: Commands and Tools
Everything you learned from Lab 1 to Lab 4 including
  Mininet
  RYU controller
  ovs-ofctl
New command: ovs-vsctl
  ovs-vsctl add bridge
    ex: sudo ovs-vsctl add bridge s1 flow_tables 0=@frank -- --id=@frank create flow_table flow_limit = 100
  sudo ovs-vsctl list bridge
  sudo ovs-vsctl list flow_table
New tool: hping3
  ex: generate TCP traffic from h1 to h2 mininet> h1 hping3 –c 40 –p ++3000 –i u50000 h2 c: count, -p: port, -i: interval

## Slide 4: Lab 5 Topology
The following topology is required in lab 5
  a costumed topology file is provided (on NYU Classes)
S1
S3
S4
S5
H1
H2
1
2
3
2
1
1
1
2
1
S2
2
2
3
4
4

## Slide 5: Lab 5 Task 1
Limit the flow table size at top-level switches
  set the flow table size to 100
use ‘ovs-vsctl’ to set flow table size = 100
S1
S3
S4
S5
H1
H2
1
2
3
2
1
1
1
2
1
S2
2
2
3
4
4

## Slide 6: Lab 5 Task 2
Write a controller that performs
  when a new TCP flow arrives, (srcIP, dstIP, srcPort, dstPort), the switch (S4 & S5) forward the first packet to controller
  controller sets up a path S4-S1-S5 for both directions
  1 flow  2 rules
src IP | dst IP | src port | dst port
X | Y | A | Z
Y | X | Z | A
S1
S3
S4
S5
H1
H2
1
2
3
2
1
1
1
2
1
S2
2
2
3
4
4

## Slide 7: Lab 5 Task 3
Use hping3 to send 100 flows (with varied dst port #) from H1 to H2
Observe flow table overflow message
  add --verbose to ryu-manager
  overflow should happen around 50 flows
hping3
S1
S3
S4
S5
H1
H2
1
2
3
2
1
1
1
2
1
S2
2
2
3
4
4

## Slide 8: Lab 5 Task 4
Modify your controller code so that
  1/3 of flows follow path S4-S1-S5
  1/3 of flows follow path S4-S2-S5
  1/3 of flows follow path S4-S3-S5
Run the same hping3 setting again to see if overflow happens
33%
S1
S3
S4
S5
H1
H2
1
2
3
2
1
1
1
2
1
S2
2
2
3
4
4
33%
33%

## Slide 9: Some hints
You still need to handle ARP message or other non-TCP packets
  hard-code ARP as you did in Lab 4
  send only TCP packets without matched entry to controller, all other packets have pre-installed path
    TCP with matched entry
    TCP without matched entry  controller
    other packets  pre-installed rule
    empty match (default)  controller
Remember to use --verbose when running ryu controller to see the overflow message
  nw_protocol and dl_type fields need to be set as we are dealing with layer 4 protocol

## Slide 10: Useful References
RYU documentation and examples
  http://ryu.readthedocs.org/en/latest/
  http://osrg.github.io/ryu-book/en/html/
hping3 usage
  http://linux.die.net/man/8/hping3
ovs-vsctl and ovs-ofctl
  http://www.pica8.com/document/v2.3/html/ovs-commands-reference/#1081533
  http://openvswitch.org/support/dist-docs/ovs-vsctl.8.txt
  http://openvswitch.org/support/dist-docs/ovs-ofctl.8.txt